## Slide 1: CSE 305 Computer Architecture Introduction
Prepared by
Madhusudan Basak
Assistant Professor
CSE, BUET

## Slide 2: Class Introduction
3 credit course
3 classes/week
  Saturday,
  Sunday and
  Tuesday
    Can be change based on previous declaration
4 Class Tests will be taken and BEST 3 will be counted

## Slide 3: Evaluation Criteria
3 credit course – Total 300 Marks
Attendance – 10%
Class Test – 20%
Term Final Exam – 70%

## Slide 4: Reference Books
Computer Organization and Design (5th Edition)
  Will be used for most of the topics
Digital Logic and Computer Design (3rd Edition)
  Will be used for some topics
Computer Systems
A Programmer’s Perspective (3rd Edition)
  Will be used for some topics

## Slide 5: Why Computer Architecture?
To apply the Architectural sense to a computer
To apply computer for Architectural design
To know about the basic Architecture of a computer

## Slide 6: Why Computer Architecture?
Purpose
  How hardware (processors, memories, disk drives, network infrastructure) plus software (operating systems, compilers, libraries, network protocols) combine to support the execution of application programs
  How you as a programmer can best use these resources

## Slide 7: Why Computer Architecture?

## Slide 8: What to know?
What the computer does
Logical View
Instruction Set Architecture (ISA)
How it does
Physical View
Computer Organization
Computer Architecture
Instruction Set Architecture
Computer Organization

## Slide 9: Instruction Set Architecture
Instruction set architecture is the attributes of a computing system as seen by the assembly language programmer or compiler.
  Instruction Set (what operations can be performed?)
  Instruction Format (how are instructions specified?)
  Data storage (where is data located?)
  Addressing Modes (how is data accessed?)
  Exceptional Conditions (what happens if something goes wrong?)

## Slide 10: Machine Organization
Machine organization is the view of the computer that is seen by the logic designer. This includes
  Capabilities & performance characteristics of functional units (e.g., registers, ALU, shifters, etc.)
  Ways in which these components are interconnected
  How information flows between components
  Logic and means by which such information flow is controlled
  Coordination of functional units

## Slide 11: Components of a Computer

## Slide 12: Components of a Computer
Control
Gives directions to the other components
e.g., bus controller, memory interface unit
Datapath
Performs arithmetic and logic operations
e.g., adders, multipliers, shifters
Memory
Holds data and instructions
e.g., cache, main memory, disk
Input
Sends data to the computer
e.g., keyboard, mouse
Output
Gets data from the computer
e.g., screen, sound card

## Slide 13: Information in a computer -- Instructions
Instructions specify commands to
  Transfer information within a computer
    e.g., from memory to ALU
  Transfer of information between the computer and I/O devices
    e.g., from keyboard to computer, or computer to printer
  Perform arithmetic and logical operations
    e. g., add two numbers, perform a logical AND

## Slide 14: Information in a computer -- Instructions
A sequence of instructions to perform a task is called a program, which is stored in the memory.
Processor fetches instructions from the memory and performs the operations stated in those instructions.
What do the instructions operate upon?

## Slide 15: Information in a computer -- Data
Data are the “operands” upon which instructions operate.
Data could be:
  Numbers,
  Encoded characters.
Data, in a broad sense means any digital information.
Computers use data that is encoded as a string of binary digits called bits.

## Slide 16: Classes of Computers
Desktop / Notebook Computers
  Low-end systems, high performance workstations.
  Subject to cost/performance tradeoff
Server Computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized
Embedded Computers
  Hidden as components of systems
  Minimize memory and power. Often not programmable

## Slide 17: Eight Great Ideas in Computer Architecture
Design for Moore’s Law
Use Abstraction to Simplify Design
Make the Common Case Fast
Performance via Parallelism
Performance via Pipelining
Performance via Prediction
Hierarchy of Memories
Dependability via Redundancy

## Slide 18: Design for Moore’s Law
Provided by Gordon Moore (co-founder of Intel) in 1965
Moore's law is the observation that the number of transistors in a dense integrated circuit (IC) doubles about every two years.

## Slide 19: Use Abstraction to Simplify Design
Computing system maintains a hierarchical structure
Lower-level details are hidden to the higher levels
Higher level only gets the abstract view
Both Hardware and Software consist of hierarchical layers using abstraction

## Slide 20: Make the Common Case Fast
More efficiency in common case, more impact in overall design.

## Slide 21: Performance via Parallelism
Current multi processor system exploits parallelism.
Often needs special care for coordination.
x = a + b
y = c*d
x = a + b
y = x*d

## Slide 22: Performance via Pipelining
Pipelining
  A special case of parallelism
  Performing multiple non-dependent operations at the same time
A
B
C

## Slide 23: Performance via Prediction
Perform operation just based on prediction/assumption
Applicable when the impact is not costly

## Slide 24: Hierarchy of Memories
We want faster and cheaper memory
Faster memory is costlier
Cheaper memory is slower
Trade-off is memory hierarchy

## Slide 25: Dependability via Redundancy
Redundancy means keeping multiple copies
One fails, another exists => Dependable

## Slide 26: Hierarchical Structure of Program Execution
Simplified view including Hardware
e.g., MS Word, Powerpoint
e.g., Compiler, Operating System
e.g., CPU, HDD, RAM

## Slide 27: Software Abstraction
Hierarchical structure for a
program execution
A + B
Add A, B
1000110010100000

## Slide 28: Hardware Abstraction: Memory
Memory Hierarchy
CPU Registers
Main Memory
(DRAMS)
Optical Disks
Cache Memory
(SRAMS)
Magnetic Disks
Magnetic Tapes
Volatile
Non-Volatile
Increased speed and cost

## Slide 29: Simplified overall abstraction
Processor
Main Memory
I/O Devices
Hardware
Compiler, Assembler, Linker, Loader
Operating System
Application Software
Executable Program
Process
File
Virtual Memory
Instruction Set Architecture
Executable Program
Executable Program
Application S/W

## Slide 30: Performance
What is the metric of the performance of a computing system?
Depends on the purpose
Two commonly used metrics are:
  Execution or Response Time
    How long it takes to do a task
  Throughput
    Total work done per unit time
      e.g., tasks/transactions/… per hour
Are these two same?

## Slide 31: Example
Do the following changes to a computer system increase throughput, decrease response time, or both?
  Replacing the processor in a computer with a faster version
    Response time decreases or improves
    Decreasing response time generally increases throughput
  Adding additional processors to a system that uses multiple processors for separate tasks—for example, searching the web
    Throughput increases
    Response time depends on scenario
      Generally no impact on response time
      But in case tasks were waiting in the queue previously, response time will decrease after the change

## Slide 32: Relative Performance
We shall focus on Response or Execution time
“X is times faster than Y” means
Example: Time taken to run a program
  A: 10s, B=15s
  So, A is 1.5 times faster than B

## Slide 33: Measuring Execution Time
Elapsed time
  Counts everything (disk and memory accesses, I/O, operating system overhead etc.)
  A useful number, but often not good for comparison purposes
    Time sharing among multiple programs
CPU time
  Doesn’t count I/O or time spent in running other programs
  Can be broken into system CPU time and user CPU time
Our focus: user CPU time
  CPU time spent in executing the lines of code that are “in” our program

## Slide 34: Clock Cycles
Time is not continuous, rather discrete to a Computer’s perspective
Activities are performed during the discrete clock ticks
cycle time = time between ticks = seconds per cycle
clock rate (frequency) = cycles per second (1 Hz. = 1 cycle/sec) A 2 Ghz. clock has a 1 / 2×109 = 0.5 nano-second (ns) cycle time
So, for a program
time

## Slide 35: Clock Cycles
For a program
Performance improvement means
  Decreasing number of clock cycles
  Increasing clock rate
  Hardware designer often trade off clock rate against cycle count

## Slide 36: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 37: Instructions vs Cycles
Is the number of cycles identical with the number of instructions?
No!

## Slide 38: Why?
Operations take different time
  Multiplication takes longer than addition
  Floating point operations take longer than integer operations
  The access time to a register is much shorter than to memory location

## Slide 39: Instruction Count and CPI

## Slide 40: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
CPI is an average since the number of cycles per instruction varies from instruction to instruction
CPI varies by application, as well as among implementation with the same instruction set
  Number of cycles for each instruction
  Frequency of instructions (instruction mix)
  Memory access time

## Slide 41: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 42: Program Execution time

## Slide 43: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 44: Performance Summary
The BIG Picture
Performance depends on
  Algorithm
  Programming language
  Compiler
  Instruction set architecture

## Slide 45: Tradeoffs
Instruction count, CPI, and clock cycle present tradeoffs
  RISC – reduced instruction set computer (MIPS)
    Simple instructions
    Higher instruction counts for an application
    Lower CPI
  CISC – complex instruction set computer (IA-32)
    More complex instructions
    Lower instruction counts for an application
    Higher CPI

## Slide 46: Comparing Computing Systems
Comparing systems => comparing execution time of the workload is required
Benchmarks can also help to evaluate measure the performance
12 benchmarks of SPECINTC2006 are given in the next slide
SPECratio can be used to measure the performance
The geometric mean of the SPECratios (of the Benchmarks) can be calculated

## Slide 47: Benchmarks

## Slide 48: Fallacies and Pitfalls
Fallacy
  Commonly held misconceptions
Pitfall
  a hidden or unsuspected danger or difficulty
  Easily made mistakes

## Slide 49: Fallacies
Fallacy 1
Fallacy 2
Computers at low utilization use little power
Designing for performance and designing for energy efficiency are unrelated goals

## Slide 50: Pitfalls
Pitfall 1
Pitfall 2
Expecting the improvement of one aspect of a computer to increase overall performance by an amount proportional to the size of the improvement.
  Using a subset of the performance equation as a performance metric.

## Slide 51: Amdahl’s Law

## Slide 52: Example
Suppose a program runs in 100 seconds on a computer, with multiply operations responsible for 80 seconds of this time. How much do I have to improve the speed of multiplication if I want my program to run five times faster?

## Slide 53: Acknowledgements
These slides contain material developed and copyright by:
  Krste Asanovic (UCB), James Hoe (CMU), Li-Shiuan Peh (MIT), Sudhakar Yalamanchili (GATECH), and Amirali Baniasadi (UVIC) in part of their respective courses
  Lecture slides by Dr. Tanzima Hashem, Professor, CSE, BUET
  Lecture slides by Ms. Mehnaz Tabassum Mahin, Assistant Professor, CSE, BUET

## Slide 54: Thank You 