## Slide 1: Chapter 5
Large and Fast: Exploiting Memory Hierarchy

## Slide 2: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data
§5.1 Introduction

## Slide 3: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 4: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 5: Basic Structure of Memory Hierarchy Levels

## Slide 6: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
How do we know if the data is present?
Where do we look?

## Slide 7: Direct Mapped Cache
Location determined by address
Direct mapped: A cache structure in which each memory location is mapped to exactly one location in the cache.
Mapping to a find a memory block in the cache =
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits

## Slide 8: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 9: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
22,
26,
22,
26,
16,
3,
16,
18,
16

## Slide 10: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
22,
26,
22,
26,
16,
3,
16,
18,
16

## Slide 11: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010
22,
26,
22,
26,
16,
3,
16,
18,
16

## Slide 12: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010
22,
26,
22,
26,
16,
3,
16,
18,
16

## Slide 13: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000
22,
26,
22,
26,
16,
3,
16,
18,
16

## Slide 14: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010
22,
26,
22,
26,
16,
3,
16,
18,
16
010 | Y | 11 | Mem[11010]

## Slide 15: Address Subdivision

## Slide 16: Total bits in a cache
32-bit addresses
A direct-mapped cache
The cache size is 2n blocks
  so n bits are used for the index
The block size (b) is 2m words (2m+2 bytes = 2m+2+3 bits)
  m bits are used to access the words within the block
  two bits are used for the byte part of the address
Total number of bits (C)
  C = 2n x (b + t + v)
  t = 32 – (n + m + 2)
  b = 2m+5
C = 2n x (2m+5 + 32 – (n + m + 2) + 1) = 2n x (2m x 32 + 32 –n - m -1)
v is the valid field size, i.e., 1
Size of
tag field
Block
size

## Slide 17: Total bits in a cache
How many total bits are required for a direct-mapped cache with 16 KiB of data and 4-word blocks (i.e., 16 bytes), assuming a 32-bit address?
16 KiB = 4 Ki Words = 1 Ki Blks = 210 Blks
C = 1024 x (b + t + v) = 1024x(4x32 + t + 1) = 1024x(4x32 +18+1) = 147 Kilo bits
n
Tag
Index
Offset
0
3
4
13
14
31
4 bits
10 bits
18 bits

## Slide 18: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = ⎣1200/16⎦ = 75
Block number = 75 modulo 64 = 11
⎣byte address /
bytes per block⎦
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
16 bytes
64 blocks
Byte Address

## Slide 19: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = ⎣1200/16⎦ = 75
Block number = 75 modulo 64 = 11
In fact Block 11 maps all addresses between 1200 and 1215.
⎣byte address /
bytes per block⎦
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
Byte Address

## Slide 20: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks ⇒ fewer of them
    More competition ⇒ increased miss rate
Larger miss penalty
  Larger blocks ⇒ Larger transfer time
  Can override benefit of reduced miss rate
  Early restart critical-word-first can help

## Slide 21: Early restart
resume execution as soon as the requested word of the block is returned; Does not wait for the entire block
For instruction access, it works best
  Instruction accesses are largely sequential
  so if the memory system can deliver a word every clock cycle, the processor may be able to restart operation when the requested word is returned, with the memory system delivering new instruction words just in time.
  This technique is usually less effective for data caches because it is likely that the words will be requested from the block in a less predictable

## Slide 22: Critical Word First
Organizes the memory so that the requested word is transferred from the memory to the cache first.
The remainder of the block is then transferred, starting with the address after the requested word and wrapping around to the beginning of the block.
Can be slightly faster than early restart
but it is limited by the same properties that limit early restart.

## Slide 23: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 24: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 25: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 26: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block
  (See next slides)
Write allocate
No Write
allocate

## Slide 27: Advantage for write-through
we can write the data into the cache and then read the tag;
if the tag mismatches, then a miss occurs.
Because the cache is write-through, the overwriting of the block in the cache is not catastrophic
  memory has the correct value and we can do it right.
THIS CANNOT BE DONE FOR WRITE BACK

## Slide 28: Write Back
If we have a cache miss, we must first write the block back to memory if the data in the cache is modified.
stores require two cycles:
  a cycle to check for a hit
  followed by a cycle to actually perform the write
Alternative: Write Buffer to hold that data

## Slide 29: Write Back- Write Buffer
write buffer holds the data to write in
effectively allowing the store to take only one cycle by pipelining it:
  When a store buffer is used, the processor does the cache lookup and places the data in the store buffer during the normal cache access cycle.
  Assuming a cache hit, the new data is written from the store buffer into the cache on the next unused cache access cycle.

## Slide 30: Write Back- Write Buffer for miss
the modified block is moved to a write-back buffer associated with the cache in case of a miss
  while the requested block is read from memory.
  The write-back buffer is later written back to memory.
Assuming another miss does not occur immediately, this technique reduces the miss penalty

## Slide 31: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  D-cache: write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%

## Slide 32: Example: Intrinsity FastMATH
  256 blocks × 16 words/block

## Slide 33: Measuring Cache Performance
§5.4 Measuring and Improving Cache Performance

## Slide 34: Measuring Cache Performance
For Write-through Cache

## Slide 35: Notes: Write Buffer Stalls
Write buffer stalls depend
  on the proximity of writes
  and not just the frequency
Usually we can ignore write buffer stalls
  in systems with 4 or more words depth
  With a memory capable of accepting writes at a rate that significantly exceeds the average write frequency in programs (by a factor of 2)
If a system did not meet these criteria, it would not be well designed;
  instead, the designer should have used either a deeper write buffer or a write-back organization
So not easy to
deduce an equation

## Slide 36: Measuring Cache Performance
With simplifying assumptions:
  read and write miss penalties are same
    In most write-through schemes this is the case
  Write buffer stalls are negligible
§5.4 Measuring and Improving Cache Performance
For
Data
For
Instruction

## Slide 37: Cache Performance Example
Given
  miss rate: I-cache = 2% ; D-cache = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Say total instruction: I
  I-cache miss cycles: I × 0.02 × 100 = 2.00 × I
  D-cache: I × 0.36 × 0.04 × 100 = 1.44 × I
Actual CPI = 2 + 2 + 1.44 = 5.44
Ideal CPU is 5.44/2 =2.72 times faster
How much
faster is a
processor
with a perfect
cache?

## Slide 38: Amdahl’s Law
A rule stating that the performance enhancement possible with a given improvement is limited by the amount that the improved feature is used.
What happens if the processor is made faster, but the memory system is not?
  The amount of time spent on memory stalls will take up an increasing fraction of the execution time

## Slide 39: Cache Performance Example 2
Given
  miss rate: I-cache = 2% ; D-cache = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 1
  Load & stores are 36% of instructions
Say total instruction: I
  I-cache miss cycles: I × 0.02 × 100 = 2.00 × I
  D-cache: I × 0.36 × 0.04 × 100 = 1.44 × I
Actual CPI = 1 + 2 + 1.44 = 4.44
Ideal CPU is 4.44/1 =4.44 times faster
How much
faster is a
processor
with a perfect
cache?

## Slide 40: Lesson (re)Learned
Previously
it was 5.44
Performance lost increases

## Slide 41: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 42: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 43: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 44: Associative Cache Example

## Slide 45: 1-Way Set Associative
A cache block can only go in one spot in the cache.
It makes a cache block very easy to find
but it‛s not very flexible about where to put the blocks.
How many bits?
3 bits

## Slide 46: 2-Way Set Associative
This cache is made up of sets that can fit two blocks each.
The index is now used to find the set
The tag helps find the block within the set.
How many bits?
2 bits

## Slide 47: 4-Way Set Associative
Each set here fits four blocks,
So there are fewer sets.
As such, fewer index bits are needed.
How many bits?
1 bit
0 1

## Slide 48: Fully Associative
No index is needed, since a cache block can go anywhere in the cache.
Every tag must be compared when finding a block in the cache
but block placement is very flexible!
How many bits?
0 bit

## Slide 49: Spectrum of Associativity
For a cache with 8 entries

## Slide 50: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
0 modulo 4 = 0
8 modulo 4 = 0
0 modulo 4 = 0
6 modulo 4 = 2
8 modulo 4 = 0

## Slide 51: Associativity Example
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
2-way set associative
0 modulo 2 = 0
8 modulo 2 = 0
6 modulo 2 = 0
8 modulo 2 = 0
0 modulo 2 = 0

## Slide 52: Associativity Example
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Fully associative

## Slide 53: Set Associative Cache Organization
4-Way
Enable
Signals
An Alternate
Implementation:
Remove
the multiplexor

## Slide 54: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 55: Tags versus Set Associativity
Cache of 4096 blocks
a 4-word block size
32-bit address,
Find the total number of sets and the total number of tag bits for caches that are
  direct mapped
  two-way set associative
  four-way set associative
  fully associative.

## Slide 56: Tags versus Set Associativity
28 bits (tag + Index) | 4 bits
16 bit tag | 12 bit index | 4 bits
4096 blocks; 32 bit address
4 words block = 16 (24) Bytes block
So for tag + index 32 – 4 = 28 bits
Direct Mapped:
  4096 (212) 1-way set => 12 bit index
  16 bit tag (28 -12)
  4096 entries × 16 bit tag = 64 K bits tag

## Slide 57: Tags versus Set Associativity
28 bits (tag + Index) | 4 bits
4096 blocks; 32 bit address
4 words block = 16 (24) Bytes block
So for tag + index 32 – 4 = 28 bits
2-way set associative :
  4096/2 = 2048 (211) sets => 11 bit index
  17 bit tag (28 -11)
  4096 entries × 17 bit tag = 68 K bits tag
17 bit tag | 11 bit index | 4 bits

## Slide 58: Tags versus Set Associativity
28 bits (tag + Index) | 4 bits
4096 blocks; 32 bit address
4 words block = 16 (24) Bytes block
So for tag + index 32 – 4 = 28 bits
4-way set associative :
  4096/4 = 1024 (210) sets => 10 bit index
  18 bit tag (28 -10)
  4096 entries × 18 bit tag = 72 K bits tag
18 bit tag | 10 bit index | 4 bits

## Slide 59: Tags versus Set Associativity
Fully set associative :
  No index
  28 bits tag (28 - 0)
  4096 entries × 28 bit tag = 112 K bits tag
28 bits (tag + Index) | 4 bits
4096 blocks; 32 bit address
4 words block = 16 (24) Bytes block
So for tag + index 32 – 4 = 28 bits
28 bit tag | 4 bits

## Slide 60: Tags versus Set Associativity
4096 blocks; 4-words block; 32-bit address
4-words block = 16 (24) Bytes block
So, for tag + index has 32 – 4 = 28 bits.
28 bits (tag + Index) | 4 bits
Associativity | Tag bits (K)
Direct mapped (1 Way) | 64
2 Way Set Associative | 68
4 Way Set Associative | 72
Fully Associative | 112

## Slide 61: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 62: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction @ primary cache = 2%
  Main memory access time = 100ns
  4 GHz => 0.25ns cycle length
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 63: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6
  CPU base CPI = 1,
  clock rate = 4GHz
  primary Miss rate = 2%

## Slide 64: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 65: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation

## Slide 66: Dependability
Fault: failure of a component
  May or may not lead to system failure
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration
§5.5 Dependable Memory Hierarchy

## Slide 67: Dependability Measures
Reliability: mean time to failure (MTTF)
Service interruption: mean time to repair (MTTR)
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair

## Slide 68: Nines of Availability
We want availability to be very high.
One shorthand is to quote the number of “nines of availability” per year.
# of Nines | % of uptime
One | 90
Two | 99
Three | 99.9
Four | 99.99
Five | 99.999

## Slide 69: Nines of Availability
Given 365 days per year, which is 365 * 24 * 60 = 525,600 minutes.
Then the shorthand is decoded as follows:
90% => 525,600 * 0.1 downtime = 52560 minutes = 52560/(60*24) = 36.5 days.
# of Nines | % of uptime | Downtime/Year
One | 90 | 36.5 days
Two | 99 | 3.65 days
Three | 99.9 | 526 min
Four | 99.99 | 52.6 min
Five | 99.999 | 5.26 min

## Slide 70: MTTF and AFR
MTTF is a reliability measure.
A related term is annual failure rate (AFR)
  The percentage of devices that would be expected to fail in a year for a given MTTF.
    Hours in a year / MTTF
  When MTTF gets large it can be misleading
  while AFR leads to better intuition

## Slide 71: High MTTF and AFR
Some disks today are quoted to have a 1,000,000-hour MTTF.
  1,000,000/(365 * 24) = 114 years
  they practically never fail???
Warehouse scale computers that run Internet services such as Search might have 50,000 servers.
Assume each server has 2 disks.
How many disks we would expect to fail per year.

## Slide 72: High MTTF and AFR
One year => 365 * 24 = 8760 hours.
A 1,000,000-hour MTTF means an AFR of 8760/1,000,000 = 0.876%.
We have 50000 * 2 = 100,000 disks
we would expect 0.00876 * 100,000 = 876 disks to fail per year
On average more than (876/365) 2 disk failures per day.

## Slide 73: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault
§5.7 Virtual Memory

## Slide 74: Address Translation
Fixed-size pages (e.g., 4K)

## Slide 75: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
    But this needs costly search!!!
  Smart replacement algorithms

## Slide 76: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 77: Translation Using a Page Table
220 (= 1 M) entries
19 bits;
but 32 bits
wide usually
What is
the size
of the
page table?

## Slide 78: Page Table Size Issues
Size of page table => 4 MB (per process)
What about 100 processes
  Each with its own page table?
What will happen if we have 64-bit addresses (according to prev. calc.)?
  2(64 – 12) = 252 entries!!!
  There are techniques to reduce the amount of storage required for the page table.
52 bits | 12 bits
63………………………………………………………………………………………………….12 11………………….0

## Slide 79: Techniques: Limit Registers
Keep a limit register that restricts the size of the page table for a given process.
  If the virtual page number becomes larger than the contents of the limit register, entries must be added to the page table.
  This technique allows the page table to grow as a process consumes more space.
    Thus, the page table will only be large if the process is using many pages of virtual address space.
  This technique requires that the address space expand in only one direction.

## Slide 80: Techniques: Limit Registers
Limit Register

## Slide 81: Techniques: Two Limits
Two separate page tables and two separate limits.
  One grows from highest address down
  One grows from lowest address up
  So, address space is divided into 2 segments.
  High-order bit of an address usually determines which segment
    i.e., which page table to use for that address.
  So, each segment can be as large as one-half of the address space.
  A limit register for each segment specifies the current size of the segment, which grows in units of pages.
Stack
Allowing growth in only one direction is not sufficient
Heap

## Slide 82: Techniques: Inverted Page Table
Keep only one entry per physical block (i.e., frame)
Such a structure is called an inverted page table.
  we can no longer just index the page table.
  So, the lookup process is slightly more complex
May apply a hashing function to the virtual address
  To make the lookups faster

## Slide 83: Techniques: Multiple Levels
The first level maps large fixed-size blocks of virtual address space
Each entry in the segment table:
  indicates whether any pages in that segment are allocated
  if so, points to a page table for that segment.
Address translation happens:
  by first looking in the segment table, using the highest-order bits of the address.
  If the segment address is valid, the next set of high-order bits is used to index the page table
Sometimes called segment

## Slide 84: Techniques: Multiple Levels

## Slide 85: Mapping Pages to Storage

## Slide 86: Page Fault
If the valid bit for a virtual page is off, a page fault occurs.
The operating system must be given control.
  This transfer is done with the exception mechanism
  OS must find the page in the next level of the hierarchy
  and decide where to place the requested page in main memory.

## Slide 87: Swap Space
Virtual addr. alone does not immediately tell us where the page is on disk.
OS usually creates the space on flash memory/disk for all the pages of a process
OS creates a data structure to record where each virtual page is stored on disk.
  may be part of the page table
  or an auxiliary data structure indexed in the same way as the page table
OS also creates a data structure that tracks
  which processes and which virtual addresses use each physical page
Swap Space

## Slide 88: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 89: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs
  Misses could be handled by hardware or software
Page Tables are
in main memory

## Slide 90: Fast Translation Using a TLB

## Slide 91: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 92: TLB Miss Handler
TLB miss indicates
  Page present, but PTE not in TLB
  Page not present
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not present, page fault will occur
The reference and dirty bits may change in TLB
  So they must also be copied back to PTE for the TLB entry that is replaced
True Page Fault
Write-Back Scheme

## Slide 93: TLB: Associativity
Some systems use small, fully associative TLBs
  replacement choice becomes tricky
    hardware LRU scheme is too expensive.
    expensive software algorithm is also not feasible (unlike page faults)
    Many systems provide some support for randomly choosing an entry to replace.
Other systems use large TLBs, often with small associativity.
Lower Miss Rate
Not so high search cost
TLB misses are much more frequent

## Slide 94: Page Fault Handler
Use faulting virtual address to find PTE
Locate page on disk
Choose page to replace
  If dirty, write to disk first
Read page into memory and update page table
Make process runnable again
  Restart from faulting instruction

## Slide 95: Intrinsity FastMATH TLB
4 KiB (212) pages; 32-bit address space
  So, virtual page number is (32 – 12 =) 20 bits long
  Physical address is same size as virtual address.
TLB: 16 entries; fully associative
  shared between the instruction and data
  Each entry is 64 bits wide
    a 20-bit tag (virtual page number for that TLB entry)
    the corresponding physical page number (also 20 bits),
    a valid bit, a dirty bit, and other bookkeeping bits.
  Like most MIPS systems, it uses software to handle TLB misses.

## Slide 96: TLB and Cache Interaction
CAM
Implementation
Cache
256 blocks × 16 words/block

## Slide 97: Content Addressable Memory (CAM)
CAM is a circuit that combines comparison and storage in a single device.
  Does not supply an address and read a word like a RAM
  you supply the data and the CAM looks to see if it has a copy and returns the index of the matching row.
  With CAMs higher set associativity in cache can be implemented

## Slide 98: Processing a read or a write-through in the Intrinsity FastMATH TLB and cache

## Slide 99: TLB, Cache and VM Events Combined

## Slide 100: Physically Addressed Cache
Here, cache is “physically addressed” and “physically tagged”
Time to access memory for a cache hit include:
  TLB access time
  Cache access time
Of course, these accesses can be pipelined.

## Slide 101: Virtually Indexed Cache
Alternatively, the processor can index the cache with a virtual address
  Virtually indexed and Virtually tagged cache
Here, TLB is unused during the normal cache access
  Reduce cache latency
Cache miss=> the processor needs to translate the address to a physical address
  so that it can fetch the cache block from main memory.
VIVT

## Slide 102: Aliasing in VIVT Cache
Aliasing occurs when the same object has two names
  Two virtual addresses for the same page.
  May happen for shared pages between processes
  This ambiguity creates a problem:
    A word on such a page may be cached in two different locations, each corresponding to different virtual addresses.
    One program may write the data without the other program being aware that the data had changed.
Solution to Aliasing Issues
  either introduce design limitations on the cache and TLB to reduce aliases
  or require the operating system, and possibly the user, to take steps to ensure that aliases do not occur

## Slide 103: Virtually Indexed Physically Tagged
Physical Tag using just the page-offset portion of the address, which is really a physical address since it is not translated
These designs, which are virtually indexed but physically tagged, attempt to achieve the performance advantages of virtually indexed caches with the architecturally simpler advantages of a physically addressed cache.
  There is no alias problem in this case.

## Slide 104: Memory Protection
Different tasks can share parts of their virtual address spaces
  But need to protect against errant access
  Requires OS assistance
Hardware support for OS protection
  Privileged supervisor mode (aka kernel mode)
  Privileged instructions
  Page tables and other state information only accessible in supervisor mode
  System call exception (e.g., syscall in MIPS)

## Slide 105: Memory Protection: H/W Suport
Need to Support:
  at least two modes:
    Privileged supervisor mode (aka kernel mode)
    User mode
  Different Processor states:
    Allow for a process to read only; No Write allowed
    To write, privileged instructions are needed that are only available in supervisor mode
    Page tables and other state information only accessible in supervisor mode
  System call exception (e.g., syscall in MIPS):
    This allows a process to change mode:
      User mode => supervisor mode (and vice versa)

## Slide 106: Memory Protection
Each process has its own virtual address space.
OS can keep the page tables organized so that the independent virtual pages map to disjoint physical pages
  one process will not be able to access another’s data.
But what if the Process changes the mapping?
Page tables are placed in the protected address space of the OS
  So, user process is refrained from changing the page table mapping.
  But OS is able to modify the page tables.

## Slide 107: Memory Sharing and Protection
OS assists processes for limited information sharing
  OS can change the Page table as needed
  The write access bit is used to restrict write
    Can be changed only by OS
Example:
P2 wants P1 to access its page
P2 asks OS to create a page table entry for a virtual page in P1’s address space that points to the same physical page that P2 wants to share.
Any bits that determine the access rights for a page must be included in both the page table and the TLB because the page table is accessed only on a TLB miss.

## Slide 108: Memory Protection: Context Switch
Context Switch: A changing of the internal state of the processor to allow a different process to use the processor
Suppose a context switch has occurred:
  P1 was running; now P2 will run
  OS must ensure that P2 cannot get access to P1’s page tables
    Page Table register is changed
  What about the TLB?
  OS must clear the TLB entries that belong to P1
    to protect the data of P1 and
    to force the TLB to load the entries for P2.
    If the process switch rate were high, this could be quite inefficient especially if context switch is frequent.

## Slide 109: Memory Protection: Context Switch
A common alternative:
extend the virtual address space by adding a process identifier or task identifier.
The Intrinsity FastMATH has an 8-bit address space ID (ASID) field for this purpose.
  This small field identifies the currently running process
  it is kept in a register loaded by OS when it switches processes.
  The process identifier is concatenated to the tag portion of the TLB
  TLB hit occurs only if both the page number and the process identifier match.
  This eliminates the need to clear the TLB in context switch
Similar problems can occur for a cache, since on a process switch the cache will contain data from the running process.

## Slide 110: Exception Enable/Disable
Suppose we have a page fault exception and OS is handling it
What will happen, if a second exception occurs?
  The control unit would overwrite the exception program counter, making it impossible to return to the instruction that caused the page fault!
We need the ability to disable and enable exceptions.
When an exception first occurs, the processor sets a bit that disables all other exceptions;
this could happen at the same time the processor sets the supervisor mode bit.
The OS will then save just enough state to allow it to recover if another exception occurs
  the exception program counter (EPC) and Cause registers
  The operating system can then re-enable exceptions.

## Slide 111: Special control registers that help with exceptions, TLB misses, and page faults
When a TLB miss occurs, the MIPS hardware saves the page number of the reference here.

## Slide 112: TLB Miss in MIPS
TLB Miss exception invokes OS, which handles the miss in software.
Control is transferred to 8000 0000hex (TLB Miss Handler Address)
To find the physical address for the missing page, the TLB miss routine indexes the page table using the page number of the virtual address and the page table register
To make this indexing fast, MIPS hardware places the address of the Page Table Entry in a special Context Register
Thus, the first two instructions copy the Context register into the kernel temporary register $k1 and then load the page table entry from that address into $k1.
Recall that $k0 and $k1 are reserved for the operating system

## Slide 113: TLB Miss in MIPS
TLB miss handler does not check to see if the page table entry is valid.
If invalid, another and different exception occurs, and OS recognizes the page fault.
  (frequent) TLB miss becomes fast
  at a slight performance penalty for the (infrequent) page fault.
it transfers
control to
8000 0180h

## Slide 114: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
§5.8 A Common Framework for Memory Hierarchies
The BIG Picture

## Slide 115: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 116: Finding a Block
Hardware caches
  Reduce comparisons to reduce cost
Virtual memory
  Full table lookup makes full associativity feasible
  Benefit in reduced miss rate
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 117: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support

## Slide 118: Write Policy
Write-through
  Update both upper and lower levels
  Simplifies replacement, but may require write buffer
Write-back
  Update upper level only
  Update lower level when block is replaced
  Need to keep more state
Virtual memory
  Only write-back is feasible, given disk write latency

## Slide 119: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 120: Cache Design Trade-offs
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. Very large block could increase miss rate.

## Slide 121: Cache Control
Example cache characteristics
  Direct-mapped, write-back, write allocate
  Block size: 4 words (16 bytes)
  Cache size: 16 KB (1024 blocks)
  32-bit byte addresses
  Valid bit and dirty bit per block
  Blocking cache
    CPU waits until access is complete
§5.9 Using a Finite State Machine to Control A Simple Cache
Tag
Index
Offset
0
3
4
9
10
31
4 bits
10 bits
18 bits

## Slide 122: Interface Signals
Cache
CPU
Memory
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
32
32
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
128
128
Multiple cycles per access

## Slide 123: Finite State Machines
Use an FSM to sequence control steps
Set of states, transition on each clock edge
  State values are binary encoded
  Current state stored in a register
  Next state = fn (current state, current inputs)
Control output signals = fo (current state)

## Slide 124: Cache Controller FSM
Could partition into separate states to reduce clock cycle time